## Slide 1
Lab 4 Keypad
Dr. Jingtong Hu
Department of Electrical and Computer Engineering
Swanson School of Engineering
jthu@pitt.edu
Notes: Instructions for editing school and department titles:
Select from menu: View > Master > Slide Master
Click on each text area you wish to edit. Text will become editable.

## Slide 2: Keypad Scan

## Slide 3: Keypad Scan
Step 1: Set Output
R1,R2,R3,R4 = 0000
Step 2: Read Input
C1,C2,C3 = 111
⟹ No key pressed
0
0
0
0
1
1
1

## Slide 4: Keypad Scan
Key “0” is pressed

## Slide 5: Keypad Scan
Step 1: Set Output
R1,R2,R3,R4 = 0000
Step 2: Read Input
C1,C2,C3 = 101
⟹ Some key in 2nd column is pressed down
0
0
0
0
1
0
1

## Slide 6: Keypad Scan
Step 1: Set Output
R1,R2,R3,R4 = 0000
Step 2: Read Input
C1,C2,C3 = 101
⟹ Some key in 2nd column is pressed down
0
0
0
0
1
0
1
Which one?

## Slide 7: Keypad Scan
Step 1: Set Output
R1,R2,R3,R4 = 0000
Step 2: Read Input
C1,C2,C3 = 101
Step 3a: Scan 1st row
R1,R2,R3,R4 = 0111
C1,C2,C3 = 111
⟹ No key in 1st row
is pressed down
0
1
1
1
1
1
1
Scan 1st row

## Slide 8: Keypad Scan
Step 1: Set Output
R1,R2,R3,R4 = 0000
Step 2: Read Input
C1,C2,C3 = 101
Step 3b: Scan 2nd row
R1,R2,R3,R4 = 1011
C1,C2,C3 = 111
⟹ No key in 2nd row
is pressed down
1
0
1
1
1
1
1
Scan 2nd row

## Slide 9: Keypad Scan
Step 1: Set Output
R1,R2,R3,R4 = 0000
Step 2: Read Input
C1,C2,C3 = 101
Step 3c: Scan 3rd row
R1,R2,R3,R4 = 1101
C1,C2,C3 = 111
⟹ No key in 3rd row
is pressed down
1
1
0
1
1
1
1
Scan 3rd row

## Slide 10: Keypad Scan
Step 1: Set Output
R1,R2,R3,R4 = 0000
Step 2: Read Input
C1,C2,C3 = 101
Step 3d: Scan 4th row
R1,R2,R3,R4 = 1110
C1,C2,C3 = 101
⟹ key in 4th row
is pressed down
1
1
1
0
1
0
1
Scan 4th row

## Slide 11: Keypad Scan
⟹ Key pressed is located at the second column and the fourth row.
1
1
1
0
1
0
1

## Slide 12: Keypad Scan

## Slide 13: I/O Debouncing
Example signal when a button is pressed